## Slide 1: MIPS Microarchitecture

## Slide 2: Instruction Set Architectures
The ISA is one level above the physical architecture
Defines the following:
  Supported instruction and their semantics
  Supported data types
  Registers: size, number, and purpose
  Memory: layout, addressing, alignment, endiance
    Memory is an array of bytes
  OS interface:
Does not define the following:
  technology used
  chip layout
  memory implementation
  etc
Very Similar to an API:
RISC versus CISC
  Reduced Instruction Set Computer (RISC)
  Complex Instruction Set Computer (CISC)
x86
x86
ARM
MIPS
RISC Examples
AMD
endiance: the order of bytes within a word
big: 1,2,3,4 (yy/mm/dd)
little: 4,3,2,1 (dd/mm/yy)
middle: 3,4,1,2 (mm/dd/yy)
INTEL
CISC Examples
Easy Read: https://medium.com/swlh/what-does-risc-and-cisc-mean-in-2020-7b4d42c9a9de

## Slide 3: Universal Computer
TM(Q, Σ, 𝚪, 𝛅, q0)
Tape: sufficiently large
A specialized control unit (aka firmware)
A specialized program placed on tape
A generic program placed on tape
Input coming from an I/O device
h
Sufficiently Large Tape
e
l
l
o
$
$
Universal Computer
input string:
$
control unit
The OS
Your program
memory

## Slide 4: Generalized Execution Cycle
Fetch:
  Move the instruction into the control unit
Decode
  Set control lines to allow data to flow to ALU
Execute
  Activate the ALU
Writeback
  Write the data to a register or memory
Harvard Memory

## Slide 5: MIPS Microarchitecture

## Slide 6: MIPS Pipeline Execution
Instruction | Clock 1 | Clock 2 | Clock 3 | Clock 4 | Clock 5 | Clock 6 | Clock 7 | Clock 8
#1 | Fetch | Decode | Execute | Mem | WB | Fetch #6 |  | 
#2 |  | Fetch | Decode | Execute | Mem | WB |  | 
#3 |  |  | Fetch | Decode | Execute | Mem | WB | 
#4 |  |  |  | Fetch | Decode | Execute | Mem | WB
#5 |  |  |  |  | Fetch | Decode | Execute | Mem

## Slide 7: MIPS ISA Architecture: Instructions
Three basic instruction types
  Arithmetic, bitwise logic, etc.
  Data transfers
  Basic control flow
Examples:
  add $v0, $v0, $a0 # $v0 = $v0 + $a0
  addi $v0, $v0, 2 # $v0 = $v0 + 2
  srl $a0, $a1, 4 # $a0 = $a1 >>> 4
  li $t0, 4 # $t0 = 4
  move $t1, $t2 # $t1 = $t2
  lb $s0, 0($t0) # $s0 = MEM[$t0] lh $s1, 3($t0) # $s1 = concat(MEM[$t0+3+1],MEM[$t0+3+0])
  beq $t3, $t5, label # if ($t3 == $t5) goto label
  jal proc # method()
MEM
0
1
2
n-1
$t0 = 4; 0($t0) ⇔ $t0[0]
t0:
3
4

## Slide 8: MIPS ISA Architecture: Registers
Data types:
  byte, half, word
  integer (signed/unsigned), binary32, binary64
Registers:
  32: 32-bit integer registers
  32: 32-bit floating point registers
    binary32: $fp0 .. $fp31
    binary64: {$fp0, $fp1} .. {$fp30, $fp31}
  3: system registers: pc, hi, lo
Integer Registers

## Slide 9: MIPS ISA (Architecture) Memory Layout
Memory:
  memory layout
  byte addressable
  lowest address at bottom
  32-bit words
  little endian format
Little endian format
  recall 32-bit registers (4 bytes)
  fall to the left
4: DE
3: AD
2: BE
1: EF
1: EF
2: BE
3: AD
4: DE
1: EF
2: BE
3: AD
4: DE
$sp
$fp
$gp
endiance: the order of bytes within a word
big: 1,2,3,4 (yy/mm/dd)
little: 4,3,2,1 (dd/mm/yy)
middle: 3,4,1,2 (mm/dd/yy)

## Slide 10: Memory Organization (Java program)
class Main { public static int x = 5; int y = 7; public int addNumbers(int a, int b) { int sum = a + b; return sum; } public static void main(String[] args) { int num1 = 25; int num2 = 15; // create an object of Main Main obj = new Main(); int result = obj.addNumbers(num1, num2); System.out.println("Sum is: " + result); } }
.text (INSTRUCTIONS)
.data
STACK int a; int b;
HEAP
}
}
Dynamic: Locations defined at runtime.
Static: Locations are defined when the program starts.

## Slide 11: MIPS ISA Architecture: OS interface
Kernel Calls: 'syscall' instruction
Service Name | $v0 | input: $a0..$a3 | output: $v0..$v1
print integer | 1 | $a0 = value | none
read integer | 5 | none | $v0 = value
malloc | 9 | $a0 = size | $v0 = buffer address
exit | 10 | none | none
file read | 14 | $a0 = fd, $a1 = buffer address $a2 = num bytes | $v0 = bytes read -1 == error 0 == eof